## Slide 1: RV32I (no CSR &no iFence) Core
Tarun Govind Kesavamurthi
North Carolina State University
tkesava@ncsu.edu

## Slide 2: Core - source code Source - https://github.ncsu.edu/tkesava/Heterogeneous-multicore.git
riscv_ISA branch contains RV32i sources.
Scalar_cores:
    1stage_core – single cycle core
    5stage_core_riscv – 5 stage scalar core
    Simulator – functional simulator for verification (in progress)
riscv: Contains riscv ISA spec and RV32i supported instructions list xls
Programs:
    C : riscv_test – riscv ISA compliance tests
      Common:
        Boot assembly file - init.s
        Linker script – link.ld
        Init c source file (vector table)– init1.cc
        Custom lib file – myClib
      Median
      Multiply
      Qsort
      Spmv
      * Additional riscv_tests to be ported*
    ASM : Assembly level tests

## Slide 3: 5 Stage riscv core – base

## Slide 4
Module hierarchy – As mentioned
debug_headerfile.svh – All config params of the core
+EXEC – argument for memory file
Verilator_tb
Recent updates – Optional (bimodal) branch predictor and BTB with parameterizable structure sizes

## Slide 5: Software hardware interface
CONSOLE_ADDR – “32’d65540”: address treated as console address to check the results
Linker sections
  Text : program instructions (including the bootloader instns)
  Vector : Contains static global readonly vector table
  Data : Initialized global and static data variables in the program
  Bss : Uninitialized global data variables in the program
Start of a section is stored in the symbol _s*section_name* (Eg: _stext)
End of a section is stored in the symbol _e*section_name* (Eg: _etext)

## Slide 6: Custom C library – myClib
Limited functionality: only focused to generate print statements
Methods provided in myClib (as on 09/23/2020) –
  atoi
  write_string
  write_char
See source in programs/common/myClib for the args

## Slide 7: Thread migration and 3D physical design (current work)
Idea: Migrate threads between cores like Jimmy Page playing double neck guitar.
Action plans: Create two 5-stage scalar cores and swap the threads dynamically with a thread swap controller
Putfalls:
Polluted BTB and Branch Predictor
A series of cache misses after thread swap

## Slide 8: Thread Migration Controller
Thread migration controller
Thread migration controller:
Timer in thread migration controller, which keep track of the switching time
Swap all in-flight instructions in the pipeline stages
Cache misses caused by thread migration?
Branch miss predicts caused by thread migration?
Switch the entire front end of the pipeline (fetch and decode) with a central mux.
IF
ID
MEM
WB
EX
IF
ID
MEM
WB
EX

## Slide 9: Thread Migration – HMP (with out of order super scalar cores)
iMEM
Decoder
ARF & RMT
ROB
RS
FU
FU
iMEM
Decoder
ARF & RMT
ROB
RS
FU
FU
Thread Swap Controller

## Slide 10: Thread Migration Controller
Level 1
Level 2
Average Compute & Compare
Swap_threads
Monitor the IPC of both cores
Fill the history table recording the IPC for n instruction cycles
Compute and compare the weighted average IPC recorded and make a decision

## Slide 11: Improvements and Future plans
Core:
Use SOC standard interface with the core (wishbone or AMBA – AHB etc)
Port all riscv_tests
Add base 18 CSR registers, CSR instructions and fence instruction support (additional 10 instructions)
Physical Design:
720 like Physical design and the 3D methodology flow for the core (Scalar heterogenous version)
Out of order heterogenous core development